## Slide 1
Electronic Pipette
ka
Prototype v1
Proof of Concept and Initial Hardware Integration
Kahaan Padiya

## Slide 2
The Problem with Manual Pipetting
😓 Repetitive Strain
Hundreds of pipette strokes per day cause thumb and wrist fatigue, leading to RSI in lab technicians.
📉 Human Variability
Manual force inconsistency introduces volume error. CV of manual pipetting can exceed 1–2% for small volumes.
💸 Cost of Error
Inaccurate dispensing wastes expensive reagents and can invalidate entire experiment runs.
⚡ Our Goal
Build a low-cost electronic pipette using off-the-shelf components to improve consistency.

## Slide 3
Hardware Components
01
Arduino Nano
Microcontroller brain. Stores calibration positions in EEPROM, handles serial commands (PREP / ASP / DISP) and jog control.
02
Stepper Motor + Driver
Provides precise angular positioning. The driver board enables control and handles the current requirements of the Stepper.
03
Pulley & String System
Converts rotary Stepper motion into linear plunger travel. String is routed over two force-redirector for smooth, vertical actuation.
04
Web Serial Controller
Browser-based UI (Web Serial API). No app install needed — connect over USB, calibrate endpoints, and run standard pipetting protocol.
05
Future: Pressure Switch
A limit switch at maximum plunger depth will kill the motor, protecting the mechanism and auto-detecting the blowout position.

## Slide 4
Operating Protocol
Three Physical buttons on the pipette to control each stage
PREP
PREP Button
1. Push to First Stop
Press PREP button. Stepper drives plunger to pre-aspirate position and establishes consistent volume baseline before liquid contact.
ASP
ASP Button
2. Aspirate
Press ASP button. Motor retracts plunger to calibrated aspirate depth. Immerse tip first; negative pressure draws liquid in accurately.
DISP
DISP Button
3. Dispense & Blowout
Press DISP button. Full plunger travel to second stop — dispenses volume and completes blowout, expelling all residual liquid.

## Slide 5
Two Interfaces, Two Roles
LAPTOP · One-Time Calibration
Done once. Saved permanently to EEPROM.
1
Jog UP / DOWN
Use ↑↓ buttons to manually position plunger at the desired depth.
2
Set Open Position (ZERO)
Save the resting / top-of-travel position. Plunger fully retracted.
3
Save 1st Stop (Aspirate)
Motor at the exact depth that draws the correct volume into the tip.
4
Save 2nd Stop (Blowout)
Deepest point : full plunger depression to expel all residual liquid.
Recalibrate only when needed.
VS
PHYSICAL BUTTONS (V1.1) · Daily Operation
No laptop. Just the pipette.
PREP
Push to 1st Stop
ASP
Aspirate Liquid
DISP
Dispense & Blowout
Reads positions from EEPROM at boot. Works standalone.

## Slide 6
Precision Comparison: Normal vs Electronic
Manual Pipette
Electronic Pipette (v1)
Readings taken at 520nm
0.47792
0.47687
0.47757
0.47685
0.47641
0.47592
0.54012
0.56028
0.56806
0.54440
Metric | Manual | Electronic
Average | 0.4769 | 0.5532
σ (Sigma) | 0.000733 | 0.01316
3σ | 0.00220 | 0.03948
CV % | 0.154% | 2.379%
3×CV | 0.461% | 7.136%

## Slide 7
Measurement Spread Visualised
Chart: Coefficient of Variation (%)
| Manual Pipette | Electronic Pipette (v1)
CV % | 0.1538 | 2.3786

## Slide 8
Roadmap & Future Improvements
v1.1
Pressure / Limit Switch + control buttons
In Progress
Mount a microswitch at maximum plunger depth. Arduino kills motor on trigger. Add Buttons to control Prep, aspirate and dispense.
v1.2
Auto-Calibration Mode
Planned
On boot, motor travels to limit switch to find true zero automatically. Calibration saved without manual jog steps.
v2.0
Encoder Feedback
Planned
Rotary encoder on Stepper shaft provides closed-loop position control dramatically reduces CV by eliminating string slack error.
v2.1
Volume Selection UI
Future
Add a volume input to the web controller. Software maps desired µL to encoder ticks for flexible, calibrated aspiration.

## Slide 9
Conclusion
A working proof-of-concept in a form factor that costs a fraction of commercial alternatives.
✅ Functional 3-command pipetting protocol over USB Serial
✅ EEPROM-persisted calibration — survives power cycles
✅ Web based browser controller — no install required
📊 CV of 2.38% vs 0.15% manual — improvement path identified
🔧 Pressure switch (v1.1) will fix primary source of error
Built with: Arduino Nano · Stepper Motor · Web Serial API · EEPROM · Open Hardware